CONGESTION CONTROL
PROBLEM FORMULATION

---
Network Topology:
The network topology is represented as a graph G(N, E), being N the set of network nodes, and E the set of links composing the network.
Each link e belongs to E has a single initial node denoted as a(e) and a single end node denoted as b(e), both belonging to N.
Thus, only unidirectional links are considered.

---
δ(n) is the set of all e ∈ E such that b(e) = n
    --> Basically a notation for the set of all incoming links.
Each link e ∈ E has associated a real number uₑ representing its capacity, that is, the amount of average traffic it can transfer.
    --> Capacities of all the links can be represented by a vector	u = {uₑ, e∈ E}.

---
Traffic Demands
Traffic offered to the network is composed of a D of traffic demands.
Each demand d ∈ D represents a traffic flow.
a(d) - denotes the set of one or more nodes generating the flow d (i.e., the set of all nodes generating the traffic.)
and b(d) is the set of one or more nodes where the flow is targeted. (i.e., the set of all nodes receiving the traffic.)
No node can simultaneously be source and destination of a demand (a(d) ∩ b(d) = ∅)
h(d) denotes the the actual bandwidth allocated

---
Congestion Control algorithms
Congestion control algorithms are code running in the traffic sources that computes an upper limit to the allowed rate to inject in the network.
The role of a congestion control mechanism is precisely to avoid this, enforcing two goals:
  (i) a fair bandwidth assignment among the connections and
  (ii) utilizing the network links as much as possible, but still keeping traffic losses and packet delays at acceptable levels.

---
A network of millions of users and links, with a multitude of technologies and link bandwidths ranging from Kbps to Gbps and loosely organized as an interconnection of thousands of subnetworks administered by different institutions.
The majority of the traffic in the Internet is exchanged through TCP (Transmission Control Protocol) connections between end users.
TCP congestion control is the paramount example of how it is possible to successfully adjust connection rates in a fair and scalable decentralized form.

---
NUM Model
The congestion control can be modeled as a Network Utility Maximization (NUM) problem
Let G(N,E) be a network, where N is the set of nodes and E the set of links.
The sources of traffic are the demands in a demand set D.
The traffic h(d) injected by a demand d is routed through a path p(d).
Each traffic source d has an associated utility function Ud(hd)
The basic NUM congestion control model assigns the rates h = {hd , d ∈D} that solves max(h) Σ Ud(hd)
The objective function maximizes the so-called network utility, defined as the sum of the utilities of all the demands in the network.